## Slide 1: 552: Directories
Srinivas Narayana
Fall 2020

## Slide 2
Hardware address (MAC address)
Ex: 00-15-C5-49-04-A7
Network address (IP address)
Ex: 10.1.1.104
Transport address (port)
Ex: 4096
Application address (URL)
Ex: mail.google.com
The Internet
Google’s network

## Slide 3: Where do all the addresses come from? Who assigns them, and how?

## Slide 4: Where do all the addresses come from?
You, as the user, only know the application address of your destination (google.com)

## Slide 5: Addresses and what they correspond to
Transport address (TCP/UDP port): app-level conversation
Network-level address (IP address): point of attachment
Link-level address (MAC address): device

## Slide 6: Directory Services
Directories map a name to an address
Simplistic designs
  Centralized directory
  Ask everyone (e.g., flooding in ARP)
  Tell everyone (e.g., pushing /etc/hosts)
  Fix a value a priori (e.g., dst port 80 is typically HTTP)
Scalable distributed designs
  Hierarchical namespace (e.g., Domain Name System)
  Flat name space (e.g., Distributed Hash Table)

## Slide 7: Domain Name System
requesting host
cis.poly.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.poly.edu
1
2
3
4
5
6
authoritative DNS server
dns.cs.umass.edu
7
8
TLD DNS server
Host at cis.poly.edu wants IP address for gaia.cs.umass.edu
Recursive query: #1
Iterative queries: #2, 4, 6
At your home, your Wi-Fi router typically runs the local DNS resolver.

## Slide 8: ARP: address resolution protocol
ARP table: each IP node (host, router) on the local network has table
Question: how to determine interface’s MAC address, knowing its IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.78
137.196.7.14
137.196.7.88
137.196.7.23
ARP
ARP
ARP
ARP
  Contain IP  MAC address mappings for some nodes:
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
Credit: http://gaia.cs.umass.edu/kurose_ross/ppt.htm

## Slide 9: ARP protocol in action
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
TTL
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
A broadcasts ARP query, containing B's IP addr
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
1
Source MAC: 71-65-F7-2B-08-53
Source IP: 137.196.7.23
Target IP address: 137.196.7.14
…
1
Ethernet frame (sent to FF-FF-FF-FF-FF-FF)

## Slide 10: ARP protocol in action
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
TTL
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
B replies to A with ARP response, giving its MAC address
2
Target IP address: 137.196.7.14
Target MAC address:
58-23-D7-FA-20-B0
…
2
ARP message into Ethernet frame (sent to 71-65-F7-2B-08-53)

## Slide 11: ARP protocol in action
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
TTL
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
A receives B’s reply, adds B entry into its local ARP table
3
137.196.
7.14
58-23-D7-FA-20-B0
500
ARP uses broadcasting as a method to implement a directory service

## Slide 12: Playing with DNS

## Slide 13: Playing with ARP