## Slide 1: 552: Endpoint Responsibilities
Srinivas Narayana
Fall 2020

## Slide 2
Network Attachment, Application Interfacing, and Resource Sharing

## Slide 3: Three roles of endpoint network software
Bootstrapping the host into the network
  How does the endpoint get an address?
  How does the endpoint make itself known to others?
Providing an interface to networked applications
  How do higher-level applications access the network?
  What network abstractions are provided to apps?
Distributed resource sharing
  How do endpoints participate in network resource allocation?
  Related to congestion control and medium access control

## Slide 4: (1) Bootstrapping host into network
The lowest level address is hard-wired
  The network adapter (NIC) comes with MAC address
Higher-level addresses can be statically or dynamically configured
IP address
  Statically configured, or dynamically with DHCP
TCP port
  Pick a transient value, ex. HTTP src port
  … or a value agreed upon a priori, ex. HTTP dst port such as 80
Link layer
Network
Transport
Applications
adapter

## Slide 5: Dynamic Host Configuration Protocol
arriving endpoint
DHCP server
DHCP discover
(broadcast)
DHCP offer
DHCP request
DHCP ACK
(broadcast)
Host learns IP address,
Subnet mask, Gateway address, DNS server(s), and a lease time.

## Slide 6: (2) Socket: the interface to applications
Best-effort packet delivery is a clumsy abstraction
  Applications typically want higher-level abstractions
  Messages, uncorrupted data, reliable in-order delivery
Applications interface with the network using sockets
  Stream socket: reliable stream of bytes (like a file)
  Message socket: unreliable message delivery
socket
socket
User process
User process
Operating
System
Operating
System

## Slide 7: Two Basic Transport Features
Demultiplexing: port numbers
Error detection: checksums
Web server
(port 80)
Client host
Server host 128.2.194.242
Echo server
(port 7)
Service request for
128.2.194.242:80
(i.e., the Web server)
OS
Client
IP
payload
detect corruption

## Slide 8: Demultiplexing using sockets
A socket is associated with five pieces of information:
  Source and destination IP address
  Source and destination port
  Kind of transport protocol (e.g., TCP/UDP)
Together referred to as the connection five-tuple
Operating system performs a connection lookup using the 5-tuple to send incoming data to the right application
socket
socket
User process
User process
Operating
System
Operating
System

## Slide 9: Two Main Transport Layers
User Datagram Protocol (UDP)
  Just provides demultiplexing and error detection
  Header fields: port numbers, checksum, and length
  Low overhead, good for query/response and multimedia
Transmission Control Protocol (TCP)
  Adds support for a “stream of bytes” abstraction
  Retransmitting lost or corrupted data
  Putting out-of-order data back in order (reassembly)
  Preventing overflow of the receiver buffer
  Adapting the sending rate to alleviate congestion
  Higher overhead than UDP; good for most stateful applications
There are other (less popular) transports, too, e.g., DCCP
https://www.anmolsarma.in/post/dccp/
Reliable delivery, and other guarantees, are ultimately the endpoint’s responsibility, not the network’s.

## Slide 10: (3) Distributed sharing of the network
A best-effort network can easily get overloaded
  No mechanism to “block” excess data
  Instead, excess packets are simply dropped (more later)
Examples
  Shared Ethernet medium: frame collisions
  Ethernet switches and IP routers: full packet buffers
Can quickly lead to congestion collapse
Load
Useful work
“congestion
collapse”
Increase in load that results in a decrease in useful work done.
https://tools.ietf.org/html/rfc896

## Slide 11: Endpoints adjust to congestion
End hosts adapt their sending rates in response to network conditions
Learning that the network is congested
  Shared Ethernet: carrier sense multiple access
    Medium access control
  IP network: observing end-to-end performance and back off
    Congestion control
Adapting to network contention
  Slowing down the sending rate/holding off transmitting for the greater good
  React too conservatively & reduce too little  still congested
  React too aggressively & reduce too much  degrade app performance needlessly

## Slide 12: Ethernet back-off mechanism
Carrier sense: wait for link to be idle
  If idle, start sending; if not, wait until idle
Collision detection: listen while transmitting
  If collision: abort transmission, and send jam signal
Exponential back-off: Wait random time, exponentially larger on each retry, before retransmitting
  Handle contention without knowing how many others are contending
  IMHO, one of the most powerful ideas in computer science

## Slide 13: TCP congestion control (much more later)
Additive increase, multiplicative decrease
  On packet loss, divide congestion window in half
  On success for last window, increase window linearly
time
Window
halved
Loss
Other mechanisms: slow start, fast retransmit vs. timeout loss, etc.