## Slide 1: 552: Distributed Control Planes
Srinivas Narayana
Fall 2020

## Slide 2: Recall…
Rutgers
AT&T
Sprint
Verizon
Internet composed of many autonomously administered entities (ASes)
Routing computes paths

## Slide 3
Routing
Algorithm
Traditionally:
Individual routing algorithm components in each and every router interact in the control plane
data
plane
control
plane
1
2
0111
values in arriving
packet header
3
Data plane
per-packet processing
(~ tens of nanoseconds)
Control plane
per route-change processing
(~ a few seconds)
Control & Data Planes inside a router

## Slide 4: Routing enables forwarding
Each router creates & looks packets up in its own forwarding table
  But the computation of the table is itself distributed
So, how is a forwarding table computed?
Typically, by routers running a distributed computation: the routing protocol.
Three aspects of a routing protocol:
  What outcome it computes
  What algorithm it runs
  How routers discover each other

## Slide 5: E.g.: Open Shortest Path First
Rutgers
AT&T
Sprint
Verizon
OSPF: an intra-domain routing protocol

## Slide 6: What OSPF computes
Shortest path(s) between each pair of nodes
  Separate shortest-path tree rooted at each node
  Path(s) with minimum sum of link metrics
Disadvantages
  All nodes need to agree on the link metrics
  Multipath routing is limited to “equal cost multipath”
Edge weights set by the network administrator

## Slide 7: Discovering other routers: Link State ads
Each router sends out its own address and neighborhood link costs over all of its links: link state advertisement
  Each router forwards advertisements from others
  A process known as link state flooding
As long as the neighboring router and the link to it are alive, the link cost is included in the flooded message
OSPF is a link state protocol: if the state of a link changes (up/down/cost change), the entire network will know

## Slide 8: OSPF link-state routing algorithm
Dijkstra’s algorithm
net topology, link costs known to all nodes due to link state broadcast
  all nodes have same info
Compute least cost paths from one node (‘source”) to all other nodes
Extract forwarding table for that (source) node
iterative: after k iterations, know least cost path to k dest.’s
Notation:
c(x,y): link cost from node x to y; = ∞ if not direct neighbors
D(v): current value of cost of path from source to dest. v
p(v): predecessor node along path from source to v
N': set of nodes whose least cost path definitively known

## Slide 9: Dijsktra’s Algorithm From Source Node u
1 Initialization:
2 N' = {u}
3 for all nodes v
4 if v adjacent to u
5 then D(v) = c(u,v)
6 else D(v) = ∞
7
8 Loop
9 find w not in N' such that D(w) is a minimum
10 add w to N'
11 update D(v) for all v adjacent to w and not in N' :
12 D(v) = min( D(v), D(w) + c(w,v) )
13 /* new cost to v is either old cost to v or known
14 shortest path cost to w plus cost from w to v */
15 until all nodes in N'
u
v
w
D(v)
D(w)
c(w,v)
…
…

## Slide 10: Dijkstra’s algorithm: example
Step
0
1
2
3
4
5
N'
u
ux
uxy
uxyv
uxyvw
uxyvwz
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 11: Constructing a forwarding table
u
y
x
w
v
z
resulting shortest-path tree from u:
v
x
y
w
z
(u,v)
(u,x)
(u,x)
(u,x)
(u,x)
destination
link
resulting forwarding table in u:

## Slide 12: Other Kinds of Routing Protocols
Distance Vector Protocols
  Don’t flood link state throughout the network: more scalable
  Exchange local vector of distances to other nodes with neighbors
  RIP, IS-IS
  Instability: a buggy router can propagate buggy info to many routers
Path Vector Protocols
  Exchange local vector of paths to other nodes with neighbors
  BGP: Border Gateway Protocol, the glue of the Internet
  Stability issues still exist! Route hijacks, blackholing, …
  Complex and prone to misconfiguration (recent CenturyLink outage)
https://www.bleepingcomputer.com/news/technology/centurylink-routing-issue-led-to-outages-on-hulu-steam-discord-more/

## Slide 13: How essential is distributed route computation?
Internet-scale: ASes are managed by different entities
  E.g., AT&T and Verzon
    Each AS with their own policies, business arrangements, etc.
  Commercial interests: ASes not willing to open proprietary details about their connectivity, topology, capabilities, …
  Very hard to get operators (or equivalently, code) from 50,000+ ISPs of the Internet to compute routes together
  An inter-AS protocol like BGP is fundamentally necessary for the Internet’s operation

## Slide 14: How essential is distributed route computation?
Within an AS: e.g., Rutgers,
  It’s conceptually possible to compute all paths centrally
    Rutgers NOC observes the entire network from one place
    Teams within Rutgers are open and willing to collaborate
  A Significant fraction of the OSPF spec is dedicated to maintenance of the distributed link state database
    Path computation is just a small part of OSPF!
    https://tools.ietf.org/html/rfc2328
So why not compute routes in a centralized fashion?