## Slide 1
Srinivas Narayana
Fall 2020
Packet Scheduling Algorithms

## Slide 2
The approach that the Internet takes to allocate resources in the network core is to use a
distributed algorithm (congestion control)
running at endpoints.
However, it also places trust in endpoints.
This allows the Internet to scale to a large # of endpoints.

## Slide 3: Endpoint algorithms are not enough!
What if an endpoint is buggy, or malicious?
We’d like the network core to do something better than best-effort

## Slide 4: Packet Scheduling Algorithms
Which packet to send next? (order)
When to send the next packet? (timing)

## Slide 5: A taxonomy
Granularity of allocation
  Per-packet vs. per-flow vs bit-by-bit
Pre-emptive vs. non-pre-emptive
  Do you interrupt the current packet/flow if another shows up?
Size-aware vs. unaware
  Do you consider flow or packet sizes in scheduling?
Class-based (strict priority) vs. shared
  Are some flows strictly higher priority than others?
Work-conserving vs. non-work-conserving
  Do you always use spare link capacity when there is demand?
4
b
4
=
=
b
4

## Slide 6: Examples of scheduling algorithms (1/N)
First-In-First-Out (FIFO) over packets
Round-robin over packets of different flows
  G, B, Y, G, B, Y, etc. regardless of arrival order
Shortest Remaining Processing Time (SRPT)
  Flow-size-aware allocation which strictly prioritizes short flows
  Variant: shortest flow first i.e., only consider (initial) remaining processing time
  A flow-size-unaware variant may predict remaining processing time using a known flow size distribution
G
B
G
Y
Y
B
G

## Slide 7: Examples of scheduling algorithms (2/N)
Processor sharing
  Assume each flow gets a fair share of the link every unit of time
  Ideal: each flow starts receiving service immediately upon arrival
Rate limiting
  Non-work-conserving: flow can’t send even if more demand than limit
Class-based strict prioritization
  Pre-determined flow classes with strict priorities over each other
  Starve low priority flows if higher priority flows are always sending

## Slide 8: Examples of scheduling algorithms (3/N)
Hierarchical policies
  Arrange scheduling policies in a tree-hierarchy
Example:
  Rate-limit A + B
  Fair-share among A and B within limit
  Fair-share among A+B and C
Complex multi-tenant isolation policies
  E.g., amazon AWS
A
B
C

## Slide 9: There’s no one optimal scheduling
Workload adaptive flow scheduling, Faisal et al. CoNEXT 2018
The best policy depends on the distribution of flows in the workload.
Suppose we consider the metric of average completion time of flows.

## Slide 10: There’s no one optimal scheduling
Workload adaptive flow scheduling, Faisal et al. CoNEXT 2018
Multiplexing
Avoids HOL blocking
Serialization
Reduces flow completion time

## Slide 11: Exercise: When does a flow finish?
Consider a mix of “long” and “short” flows arriving at a Q
  Ex: A flow may have as few as 2 packets or as many as 105
Suppose a scheduling algorithm provides each flow:
  An average per-packet delay d (e.g., 50 ms)
  An average link bandwidth share t (e.g., 10 Mbit/s)
Which among d & t determines
  when a short flow finishes?
  when a long flow finishes?

## Slide 12: Fair Queueing
ACM SIGCOMM ’89
Alan Demers, Srinivasan Keshav, and Scott Shenker

## Slide 13: An ideal to emulate: Processor sharing
Fair-share bandwidth in the most fine-grained fashion possible
  If there are N active flows, each flow gets 1/Nth of the link rate
    N varies as flows arrive and leave
  “Bit by bit round robin” (BR), also called processor-sharing
Implementing BR directly on routers is unrealistic.
  Reason: downstream router has no metadata to route the bit
…

## Slide 14: Emulate processor sharing?
How about emulating PS with round robin over packets?
Unfair! A flow can use larger packets and gain larger bandwidth
Instead, determine when a packet would finish with BR
    Depends only on packet arrival time & # of active flows
    Let’s call this the virtual finish time
FQ: Transmit packets in the order of the virtual finish times
  Buffer management: drop packet of flow with the largest backlog
Analysis and simulation of a fair queueing algorithm. Demers, Keshav, and Shenker

## Slide 15: Hardware-friendly: Deficit Round Robin
Router-friendly implementation of a WFQ scheme
Efficient fair queueing using deficit round robin, Shreedhar and Varghese ‘95

## Slide 16: Rate Limiting

## Slide 17: Providing Isolation through Rate Limiting
Used to isolate flows from each other by giving each a fixed data rate through a link
Three commonly used terms:
(long term) average rate: how many pkts can be sent per unit time (in the long run)
  crucial question: what is the interval length? 100 packets per sec or 6000 packets per min have same average, but instantaneous behaviors can be very different
peak rate: e.g., 6000 pkts per min (ppm) avg.; 1500 ppm peak rate
(max.) burst size: max number of pkts sent consecutively (with no intervening idle)

## Slide 18: Shaping and Policing

## Slide 19: Token Bucket
token bucket: limit input flow to specified burst size and average rate
Tokens generated at rate r tokens/sec, put into bucket
Bucket can hold b tokens. Tokens are not added if bucket is full
A packet can be transmitted successfully if a token is available
  Packet “picks up” the token as it leaves the router
Over interval of time t:
number of packets that leave the token
bucket is less than or equal to (r * t + b)
Average rate r
Burst size b

## Slide 20: Token Bucket Shaper vs. Policer
Shaper: there is a bucket for tokens and a packet buffer to hold packets waiting for tokens
  Packets will be dropped if the buffer is full
A token bucket policer doesn’t contain the packet buffer:
  a packet arriving while the bucket is empty is dropped right away
Bucket of tokens enables small bursts to go through unscathed
  Short flows can exceed rate limit r, since they use up the reserve in the bucket
  Long flows will fit into the rate limit r over longer periods of time, since once they use up the reserve, they are limited by the token-fill rate r

## Slide 21: Purpose of the bucket
Suppose each flow starts with a “full” bucket (b tokens)
Bucket of tokens enables small bursts to go through unscathed
Short flows can exceed rate limit r, since they can use up the reserve in the bucket
Long flows will fit into the rate limit r over their lifetime, since they cannot exceed the average token-filling rate r after using up the reserve

## Slide 22: Token Buckets are simple to implement
Each time a packet from a flow arrives, refill tokens according to gap in time and bucket size
    tokens += r * time since last packet of flow
    tokens = min(tokens, b)
Small per-flow state: r, b, timestamp, current # of tokens
  Used to build more complex metering schemes, e.g., trTCM (RFC 2698)
You can even remove the shaping packet buffer
 policer

## Slide 23: The Internet uses token bucket policers at many bottleneck links and routers.

## Slide 24: Impact of Token Bucket Policers
Flach et al., An Internet-Wide Analysis of Traffic Policing, SIGCOMM 2016

## Slide 25: Impact on TCP

## Slide 26: Policing losses impact applications
Video rebuffer rate: rebuffer time / overall watch time
Flach et al., An Internet-Wide Analysis of Traffic Policing, SIGCOMM 2016