## Slide 1
Srinivas Narayana
Fall 2020
Fast Interconnects

## Slide 2
INTERNET
Servers
Fabric
Application 1: Data center topologies

## Slide 3: Data center costs
Amortized Cost* | Component | Sub-Components
~45% | Servers | CPU, memory, disk
~25% | Power infrastructure | UPS, cooling, power distribution
~15% | Power draw | Electrical utility costs
~15% | Network | Switches, links, transit
  *3 yr amortization for servers, 15 yr for infrastructure; 5% cost of money
The Cost of a Cloud: Research Problems in Data Center Networks. Sigcomm CCR 2009. Greenberg, Hamilton, Maltz, Patel.
Notes: Source: http://web.cse.ohio-state.edu/icdcs2009/Keynote_files/greenberg-keynote.pdf

## Slide 4: Goal: Agility -- any service, any server
Ideal: Want to place workloads where server resources are available
…regardless of which services they belong to
…regardless of how they communicate with each other
Want to view DCN as a pool of compute connected by one big high-speed interconnect (“one big switch”)

## Slide 5: Application 2: High-speed routers!
Example: to interconnect servers together in a data center rack.
(Dense deployments can have 64-100 ports per switch.)
Also applicable to core routers.

## Slide 6
Building a high-speed
switching fabric

## Slide 7: A single (n X m)-port switching fabric
Different designs of switching fabric possible
Assume n ingress ports and m egress ports, half duplex links
Any ingress port may wish to communicate with any egress port

## Slide 8: A single (n X m)-port switching fabric
Circuit switch, used in telephony network switches and modern optical switches
Connect one input and output port at a time
Typically “slow” to change.

## Slide 9: A single (n X m)-port switching fabric
Packet-switched networks require faster change in the
input  output port assignment

## Slide 10: A single (n X m)-port switching fabric
Nonblocking: if input port x and output port y are both free, they should be able to connect,
…regardless of which other ports are currently connected.
If not, switch is blocking. Many “fabrics” we encounter in real life are blocking.
  Ex: Street intersections, roundabouts
Electrical/mechanical/electronic crossover

## Slide 11: Key challenge: Many ports + Nonblocking
Low-cost nonblocking crossbars are feasible for a small # ports
However, it is costly to be nonblocking with larger # ports
Suppose each crossover is as fast as each input port (rate R)
  You need n * m crossover points.
  It is often the case that n = m. The cost grows quadratically on the number of input ports
Other possibility: crossover must transition faster than the port
  … so that you can keep the number of crossovers small
  Fabric/crossover must run at aggregate rate of n*R

## Slide 12: Key principle to scale nonblocking switches
Every nonblocking switch with large # ports is built out of many nonblocking switches with a smaller # ports.
So, how do we put together many small nonblocking switches to build one large nonblocking switch?
The subject of interconnection networks

## Slide 13: 3-stage Clos network (r*n X r*n ports)
…
n X m
…
n X m
…
n X m
…
…
r switches n X m
…
m X n
…
m X n
…
m X n
…
…
r switches m X n
…
r X r
…
r X r
…
r X r
…
…
m switches r X r

## Slide 14: How Clos networks become nonblocking
if m > 2n – 2, then the Clos network is strict-sense nonblocking.
That is, any new demand between any pair of free (input, output) ports can be satisfied without re-routing any of the existing demands.
How?

## Slide 15: Need at most (n-1)+(n-1) middle stage
…
n X m
…
n X m
…
n X m
…
…
r switches n X m
…
m X n
…
m X n
…
m X n
…
…
r switches m X n
…
r X r
…
r X r
…
r X r
…
…
m switches r X r
At most n-1 existing demands

## Slide 16: Surprising result about Clos networks
if m >= n, then the Clos network is rearrangeably nonblocking
That is, any new demand between any pair of free (input, output) ports can be satisfied by suitably re-routing existing demands.
It is easy to see that m >= n is necessary
  The surprising part is that m >= n is sufficient
https://en.wikipedia.org/wiki/Clos_network#Rearrangeably_nonblocking_Clos_networks_(m_%E2%89%A5_n)

## Slide 17: Rearrangeably nonblocking Clos built with identical switches
…
n X n
…
n X n
…
n X n
…
…
n switches n X n
…
n X n
…
n X n
…
n X n
…
…
n switches n X n
…
n X n
…
n X n
…
n X n
…
…
n switches n X n

## Slide 18
Modern data center network topologies are just folded Clos topologies.

## Slide 19: How does one design a Clos DCN?
Switches are usually n X n with full-duplex links
Fold the 3-stage Clos into 2-stages
Share physical resources between ingress and egress stages
Share ports and links across the two “sides” of the middle stage

## Slide 20
…
n/2 X n/2
…
n/2 X n/2
…
n/2 X n/2
…
…
n X n full duplex
…
n/2 X n/2
…
n/2 X n/2
…
n/2 X n/2
…
…
n X n full duplex
…
n X n
…
n X n
…
n X n
…
…
n/2 switches n X n full duplex
From/to hosts
ToR/aggregation layer
ToR/aggregation layer
Spine layer

## Slide 21: Consequences of using folded Clos
2-stage high throughput data center topology
Every switch is identical in terms of # ports and link rate

## Slide 22: What about routing?
We said that the Clos topology above is rearrangeably nonblocking.
So, how to rearrange existing demands when a new packet arrives, so that it can get across as quickly as possible?
How to do it without “interference” to (ie: rerouting) other pkts?
VL2: We don’t need to rearrange anything.

## Slide 23: Valiant Load Balancing (VLB)
Designed to move data quickly for shuffling in parallel computing
Setting: Connectivity is sparse (“hypercube” topology): log n links per node in a network with n nodes
Key idea: pick a random node to redirect a message from the source, then follow the shortest path to the destination from there
Guarantee: With high probability, the message reaches its destination very quickly (log n steps)
  Practically, this means there is very less queueing in the network

## Slide 24: VLB in data center networks
VLB is more general than data center networks or Clos
  It is a form of oblivious routing
  No need to measure DCN traffic patterns before deciding on routing
  Extremely simple to implement: no global state
VLB is very handy in folded Clos topologies due to the numerous options to pick the first-hop from the ToR switch.
  Balance load across many paths
  Path from spine to destination ToR is deterministic
Very beneficial in practice
  Performance isolation: other flows don’t matter
  High capacity (“bisection bandwidth”) between any two ToR ports

## Slide 25: Is ToR-port to ToR-port high capacity enough?
VLB + Clos provides high capacity if no ToR port demands more than its bandwidth.
When might a ToR port need to service more than its port rate?
Hint: this won’t happen for traffic going from a server  ToR
  Typically, server NIC rates are <= ToR port rates

## Slide 26: Example: Web Search
TLA
MLA
MLA
Worker Nodes
………
Deadline = 250ms
Deadline = 50ms
Deadline = 10ms
A bunch of results arrive at MLAs and TLAs in a short period.
Incoming demand to a server may exceed ToR port bandwidth!
Notes: After the animation, say “this follows what we call the partition/aggregate application structure.
I’ve described this in the context of search, but it’s actually quite general
- “the foundation of many large-scale web applications.”

## Slide 27: Hose traffic model
The guarantees of VLB + Clos only hold under the hose model:
  Demands for any one ToR port (send or receive) must not exceed its bandwidth.
Very hard to enforce especially on the receiver side without sender-side rate limits.
VL2 uses TCP convergence as a way of ensuring that aggregate ToR port demand is within its bandwidth.
  Q: think about the problems this might cause…