## Slide 1: CS 352 Internet Technology
Lecture 2, Spring 2020
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 2: Course announcements
If you have a laptop, bring it to lecture
  We will do in-class exercises
  Linux or Mac operating system preferred
Meet me after lecture today, or write email to me if:
  you’re waiting for an SPN for sections 5,6,7
  you feel under-confident about your CS + programming abilities
  you might need accommodations of any sort
Sakai, course web page, Piazza will be up later today
  TAs allocated to sections soon

## Slide 3: Review of definitions
Endpoint or Host: Machine running user application
Packet: a unit of data transmission (ex: 1500 bytes)
Link: a physical communication channel between two or more machines
Router: A machine that processes packets moving them from one link to another towards a destination
Network: Collection of interconnected machines
Address: a unique name given to a machine (more later)

## Slide 4: How do machines talk?

## Slide 5: How do machines communicate?
With 1s and 0s
  Computers only deal with 1s and 0s
  So do networks
How do we transmit 1s and 0s in a network?

## Slide 6: Physical transmission on a single link
Physical signaling (light, AC voltages, etc.) are often analog
Convert bits to signals through modulation of the physical characteristics of signals: encoding
Convert signals back to digital by decoding physical signals

## Slide 7: Multi-link networks
Need a way to move data across links
We use the term switching to denote physically moving data from one link to another
Router
Router

## Slide 8: Switching schemes
Host applications transfer data containing many messages.
(1) Circuit Switching
(2) Message Switching
(3) Packet Switching

## Slide 9: Circuit switching
Provides service by setting up the full path of connected links from the origin to the destination
Example: Telephone network

## Slide 10: Circuit switching
1. Setup: Control message sets up a path from origin to destination
2. Return signal informs source that data transmission may proceed
3. Data transmission begins
4. Entire path remains allocated to the transmission (whether used or not)
5. When transmission is complete, source releases the circuit

## Slide 11: Circuit switching
Time
A
B
C
D
Data
Call accept signal
Call request signal
Data
Transmission
Time
Propagation Delay
Total transfer time
Resource reservation
delay

## Slide 12: Message switching
Each message is addressed to a destination
Header: metadata that denotes how to process a message
The message “hops” from node to node through a network while allocating only one link at a time
  Compare to circuit switching: all links reserved at the same time, regardless of use.
Analogy: Postal service

## Slide 13: Message switching
When the entire message is received at a router, the next step and link in its journey are selected
If this selected link is busy, the message waits in a queue until the link becomes free
Store and forward switching
  Router waits for all message bits to arrive on incoming link before sending the first bit on outgoing link
  Alternative: cut–through switching sends bits as they arrive

## Slide 14: Message Switching
Time
A
B
C
D
Msg
Msg
Msg
Queueing
Delay
Total transfer time
Header

## Slide 15: Packet switching
Messages are split into smaller pieces called packets
  Packets have a maximum length
  Packets are numbered and addressed
  Packets are sent through the network one at a time
Pipelining: different parts of a message concurrently transmitted over different links
  Provides higher utilization of link resources

## Slide 16: Packet switching
Time
A
B
C
D
Pkt 1
Pkt 2
Pkt 3
Pkt 1
Pkt 2
Pkt 3
Pkt 1
Pkt 2
Pkt 3
Total transfer time
Header
Queueing
Delay
Store and forward
delay

## Slide 17: The Internet uses store-and-forward packet switching.

## Slide 18: Some comparisons
(1) Header Overhead (what % of bits on the wire is metadata?)
Circuit < Message < Packet
… assuming typical messages are larger than typical packets
(2) Total Delay
Short Bursty Messages:
Packet < Circuit
Long Continuous Messages:
Circuit < Packet

## Slide 19
Telephone Network
Connection-based
Admission control
Intelligence is “in the core network”
Every service provided by the telephone company
Traffic carried by relatively few, “well-known” communications companies
Internet
Packet-based
Best effort
Intelligence is “at the endpoints”
Services provided by anyone
Traffic carried by many routers, operated by many service providers

## Slide 20: Measuring networks
Some important metrics

## Slide 21: Some definitions
Packet size: length of a packet (bits or bytes), incl. header and data
Bandwidth: For a single link, amount of data it can transmit per unit time (bits/second or Bytes/second or packets/second)
Propagation delay: Time needed to move one bit across (second)
  Imposed by the communication medium; depends on the link “length”
Transmission delay: Time from first bit@sender to last bit@sender
  Determined by link bandwidth and packet size
Queueing delay: Time that a packet waits for transmission
  Determined by contention for the link
Total packet delay: time from first bit@sender to last bit@receiver
  propagation delay + queueing delay + transmission delay for a single packet

## Slide 22
Propagation delay = time for first box to travel the length of the belt
Bandwidth = the number of boxes put on the belt per minute (“rate”)
Suppose we have N boxes in one shipment
Shipment transmission time = N / rate
  The next box is put on the belt (1/rate) minutes after the last
Total transfer time = transmission time + propagation delay
An analogy: Conveyor belt

## Slide 23: Protocols and Layering

## Slide 24: Protocols: The “rules” of networking
Protocols consist of two things
Message format
  structure of messages exchanged with a communicating endpoint
Actions
  operations upon receiving, or not receiving, messages
Example of a Skype conversation:
  Message format: English words and sentences
  Actions: when a word is heard, say “yes”; when nothing is heard for more than 3 seconds, say “are you there?”

## Slide 25: The protocols of the Internet
Defined by the Internet Engineering Task Force (IETF)
  through RFCs (“Request For Comments”)
Layering
…
FTP
HTTP
SIP
RTSP
TCP
UDP
IP
802.11
X.25
ATM
HTTPS

## Slide 26
The Internet
Rutgers campus network
Hardware address (MAC address)
Ex: 00-15-C5-49-04-A9
Network address (IP address)
Ex: 192.168.1.4
Transport address (port)
Ex: 64058
How do I identify my network interface (device)?
Whose network am I attached to?
With which app is this conversation associated?

## Slide 27
Hardware address (MAC address)
Ex: 00-15-C5-49-04-A7
Network address (IP address)
Ex: 10.1.1.104
Transport address (port)
Ex: 4096
Application address (URL)
Ex: mail.google.com
The Internet
Google’s network

## Slide 28
Software and hardware for networking are arranged in layers.
Layering provides modularity
Each layer has a distinct function
& interacts with other layers through well-defined interfaces.

## Slide 29: Modularity through layering
Link: best-effort local pkt delivery
Network: best-effort global pkt delivery
Transport: provide guarantees to apps
Apps: useful user-level functions
HTTP
FTP
TFTP
NV
TCP
UDP
IP
Ether
ATM
WiFi
…
Protocols “stacked” in endpoint and router software/hardware

## Slide 30
Link layer
Network
Transport
Applications
The Internet
Link layer
Network
Transport
Applications
The Internet
Packet takes on headers at each layer
Packet starts as an
app “payload”

## Slide 31
Link layer
Network
Transport
Applications
Link layer
Network
Transport
Applications
Link layer
Network
Link layer
Network

## Slide 32
Link layer
Network
Transport
Applications
Link layer
Network
Transport
Applications
Link layer
Network
Link layer
Network
Routers do not typically have transport or app functionality
(more on this later.)

## Slide 33: Layering
Network communication is very complex
Layering simplifies understanding, testing, maintaining
Easy to improve or replace protocol at one layer without affecting others

## Slide 34: This course will talk about TCP/IP Layering
Application
Transport
Network
Host-to-Net
…
FTP
HTTP
SIP
RTSP
TCP
UDP
IP
802.11
X.25
ATM
HTTPS