## Slide 1: The Network Layer: Router Design, Forwarding
CS 352, Lecture 13, Spring 2020
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 2: Course announcements
Project 1 grades available
  24/7 grading policy: re-grading considered until 10 PM Sunday 29th
  TAs have provided feedback on Sakai. Contact TAs for more details
Lecture and recitation logistics:
  You will have received WebEx training invitations on Piazza
  Use a wired connection if possible
  You can hear me better in a quiet environment
  Use the chat or Q&A box to ask questions any time
  Use raise hand feature during time allotted for verbal questions
  Answer WebEx polls throughout the lecture!

## Slide 3: Where we are: The network layer
Application
Transport
Network
Host-to-Net
…
FTP
HTTP
SMTP
DNS
TCP
UDP
IP
802.11
X.25
ATM
HTTPS
The network layer exists on every endpoint and router.

## Slide 4: Review of concepts
Forwarding and routing
Data plane and control plane
  Control plane can be distributed (this course) or centralized (won’t discuss)
Network-layer addresses (IP addresses)
  Primary function: identifiers for routing

## Slide 5: Poll #1
An IP address corresponds to:
  (1) the endpoint
  (2) the application
  (3) the point of attachment of the endpoint to the network
  (4) all of the above
Please use the WebEx poll feature to answer

## Slide 6: Review of concepts
Forwarding and routing
Data plane and control plane
  Control plane can be distributed (this course) or centralized (won’t discuss)
Network-layer addresses (IP addresses): identifiers for routing
Classful addressing: classes A, B, C, multicast, reserved
  Distinguished by first few bits
  Different # bits allotted to network address and host address
Classless addressing (CIDR):
  Freely change size of network (host) address
  Allocate a subset of available addresses using a subnet
Internet routing scales through hierarchy
  IP subnetworks are the zip codes of the Internet

## Slide 7: Poll #2
Given the IP address and subnet below, what is the value of X?
  (1) 11
  (2) 23
  (3) 32
  (4) none of the above
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/X

## Slide 8: Poll #3
How many hosts can this subnetwork support?
  (1) 29
  (2) 223
  (3) 232
  (4) none of the above
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/X

## Slide 9: What’s inside a router?

## Slide 10: What do routers look like?
Access routers
Core router
Data center top-of-rack switch

## Slide 11
Routing
Algorithm
Traditionally:
Individual routing algorithm components in each and every router interact in the control plane
(Distributed control plane)
data
plane
control
plane
1
2
0111
values in arriving
packet header
3
Data plane
per-packet processing
(~ tens of nanoseconds)
Control plane
per route-change processing
(~ a few seconds)
Basic components: Control & Data Planes

## Slide 12: Router architecture overview
high-speed
switching
fabric
route
processor
router input ports
router output ports
Control plane
Data plane

## Slide 13: Input port functions
line
termination
link
layer
protocol
(receive)
lookup,
forwarding
queueing
switch
fabric
Switching:
using header field values, lookup output port using forwarding table in input port memory
goal: complete input port processing at line speed (i.e., speed of the interface, say 100 Mbit/s)
queueing: if datagrams arrive faster than they can be sent via the switch fabric to the output port
physical layer:
bit-level reception
data link layer:
e.g., Ethernet
(We’ll see this later in the course)

## Slide 14: Destination-based Forwarding in the Internet
header
payload
Packet
Router
Destination Address
Outgoing Port
Dest-network
Port
Forwarding Table
Routing Lookup Data Structure
65.0.0.0/8
128.9.0.0/16
149.12.0.0/19
3
1
7

## Slide 15
Forwarding in the Internet is based on the destination IP address on packet.
There are exceptions. But Internet forwarding is mostly:
independent of the source, e.g., legitimate vs. malicious source
independent of the type of traffic, e.g., Netflix vs. web

## Slide 16: Three types of switching fabrics

## Slide 17: Output Ports
Buffering when datagrams arrive from fabric faster than the output port rate
  If buffers filled up, packets are dropped!
  Buffer management policy decides which pkts to keep and drop
Scheduling discipline chooses among queued datagrams for transmission
  Who gets priority is chosen by the scheduler
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing

## Slide 18: Poll #4
Suppose two packets arrive at a router input port. Packet 1 has (src, dst) IP address == (X, Y). Packet 2 has (src, dst) IP address == (Z, Y). Then:
  (1) The two packets are unlikely to be forwarded out of the same output port
  (2) The two packets are highly likely to be forwarded out of the same port
  (3) Not sure

## Slide 19: Poll #5
A packet is waiting to be transmitted at a buffer on the router output port. Who decides when the packet will be transmitted?
  (1) buffer manager
  (2) Packet scheduler
  (3) Forwarding table
  (4) Line termination

## Slide 20: Prefixes and IP lookup

## Slide 21: Example Forwarding Table
0
224
232-1
128.9.0.0/16
65.0.0.0
142.12.0.0/19
65.0.0.0/8
65.255.255.255
Destination IP Prefix | Outgoing Port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
65.0.0.128/25 | 4
142.12.0.0/19 | 7
IP prefix: 0-32 bits
Longest prefix match
Prefix length
128.9.16.14

## Slide 22: Prefixes can Overlap
128.9.16.0/24
128.9.176.0/24
Routing lookup: Find the longest matching prefix (the most specific route) among all prefixes that match the destination address.
0
232-1
128.9.0.0/16
142.12.0.0/19
65.0.0.0/8
128.9.16.14
Longest matching prefix

## Slide 23: Reducing Routing Table Size
service
provider
200.71.0.0
200.71.1.0
200.71.2.0
…..
200.71.255.0
200.71.0.0
200.71.1.0
200.71.2.0
…..
200.71.255.0
Routing
table
Without CIDR:
service
provider
200.71.0.0
200.71.1.0
200.71.2.0
…..
200.71.255.0
Routing
table
With CIDR:
200.71.0.0/16

## Slide 24: Hierarchical addressing: Route aggregation
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
Efficient advertisement of routing information!

## Slide 25: LPM: Announcing more specific routes
ISPs-R-Us has a more specific route to Organization 1
Longest prefix match will be used to route IP packets
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning 199.31.0.0/16
or 200.23.18.0/23”
200.23.20.0/23
Organization 2
.
.
.
.
.
.

## Slide 26: Poll #6
If the destination IP address of a packet matches three forwarding rules 128.0.0.0/16, 128.0.0.0/20, 128.0.0.0/24, which rule will the router use?
  (1) 128.0.0.0/16
  (2) 128.0.0.0/20
  (3) 128.0.0.0/24
  (4) None of the above
  (1) 128.0.0.0/16

## Slide 27: Poll #7
If an ISP owns two prefixes 128.0.0.0/16 and 128.1.0.0/16, what prefix can it legitimately advertise to the rest of the Internet?
  (1) 128.0.0.0/8
  (2) 128.0.0.0/15
  (3) 128.0.0.0/14
  (4) None of the above