## Slide 1: Internet Players
Users of applications
    Everyone (mom and pop, kids) to get something done
Network Designers
    Protocol design and implementation
    Performance, cost, scale
Internet Service Providers
    Administrators and ISPs (AT&T)
    Management, revenue, deployment
Market/businesses on the Internet
    Consumer to consumer (ebay), Business to consumer (amazon, netflix), Business to business (alibaba, importers.com,21food.com), Consumer to business (hotjobs, monster), Govt to C, Govt to B, etc.

## Slide 2: Internet service providers (ISPs)
Local ISPs: Tier 3 (cablevision)
Regional ISPs: Tier2 (internap)
Global ISPs: Tier 1 (Verizon, Sprint, AT&T, level 3, century link, Deutsche Telekom, NTT) provide access to the entire internet; connect ISP to other ISPs
Peering ISPs
  Have a mutual relationship about forwarding traffic of each others customers (no $ involved)
Transit ISPs
  Provides access to all reachable customers ($$ involved)

## Slide 3: Core Networks: ISP Tiers
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP
Local and tier- 3 ISPs are customers of
higher tier ISPs
connecting them to rest of Internet

## Slide 4: ISPs connected via Exchanges
Flatter Internet
Business models among, content provider, transit providers, and customers
Net Neutrality
Internet Inter-domain traffic By Labovitz et.al, SIGCOMM 2010

## Slide 5: Types of Networks in an Internet
Local area networks (LAN)
  Privately owned, within building
  High speed, broadcast, Ethernet
    2 to 100 Mbps
Wide area networks (WAN)
  Spans a large area
  Point-to-point, high speed fiber lines
    Long delays but very high speed links
    Several Gbps

## Slide 6: Types of Networks (cont’d)
Wireless networks
  Hosts connected by radio or infrared links
  Local area and wide area
  Satellite networks

## Slide 7: Google WAN

## Slide 8: Microsoft WAN

## Slide 9: Historical perspective
Late 1960’s: ARPAnet (4 nodes)
Early 1970’s: Aloha net, ethernet, multiple access problem
Mid-to-late 1970’s: TCP/IP, 4.2BSD
1980’s to early 1990’s: early internet growth, e-mail & file transfer dominant, NSFNET
Mid 1990s: NSFnet handed over to commercial service providers, WWW explodes
Late 90s, business models using the internet; dot-com boom and bust
Early to mid 2000s, Web 2.0, Facebook, google, Wikipedia
Future: “Embedded networks”, 5 to 10 billion devices waiting to be networked, media convergence, ubiquitous RFID tags