## Slide 1: Computer Networking: TL; DR
CS 352, Spring 2020
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 2: The protocols of the Internet
Layering and Hourglass Design
…
FTP
HTTP
SIP
RTSP
TCP
UDP
IP
802.11
X.25
ATM
HTTPS

## Slide 3: Protocol layers: Application layer
Apps closest to the user: HTTP, SMTP, multimedia
Helper protocols: DNS
Deal with human concerns
Readability of host names to reach certain services
Often, protocols are in human readable plain text too
  HTTP, SMTP, DNS
Optimized for human-perceivable performance
  The web, VoIP, mail, apps have different “optimizations” built into them

## Slide 4: Protocol layers: Transport layer
Providing guarantees for applications over a best-effort network
  Transport layer runs on hosts
Providing connectivity between applications
  Multiplex data from multiple apps going out of a given machine
  Demultiplex data coming into a machine to different apps
UDP: main function is de/multiplexing
  Also, error detection using checksums
  Simple and lightweight
TCP: reliable, in-order delivery
  Much more heavyweight

## Slide 5: Protocol layers: The transport layer
TCP reliable delivery mechanisms
  ACKnowledgments
  Timeouts
  Retransmission strategies
TCP ordered delivery mechanisms
  Sliding window
  Flow control
TCP efficiency and fairness
  Congestion control: slow start, additive increase/multiplicative decrease

## Slide 6: Protocol layers: The network layer
Providing connectivity between machines across the Internet
  Data plane: Moving data from point to point
  Control plane: compute how data plane should move data
Network layer runs on every host and every router
Main issues: (1) Addressing
  Machine addresses aren’t necessarily human friendly (ex: IPv4/v6)
  Addresses associated with network interfaces, not hosts

## Slide 7: Protocol layers: The network layer
Main issues: (2) Router design
  High performance data movement between different network interfaces
  High-speed destination-based forwarding
  Longest-prefix-based matching
Main issues: (3) Routing
  Link-state, distance-vector, path-vector routing
  Must try to avoid suboptimal paths and routing loops
  Try to compute and converge fast
Main issues: (4) QoS
  Resolve contention at router queues
  Priority queueing, fair queueing, leaky buckets, token buckets

## Slide 8: Protocol Layers: The link layer
Provide connectivity between machines over the physical medium
  A co-ax cable, optic fiber, the air inside a room
Main issues: (1) Data encoding
  Must translate bits 0-1 from software into physical signals
Main issues: (2) Error detection
  the media are not without fault!
  Parity bits

## Slide 9: Protocol layers: The link layer
Main issues: (3) Multiple access
  Partitioning the medium’s resources
  Random access protocols: exponential back-off
  Taking turns
Main issues: (4) Handling nuances of wireless media
  Fading, hidden terminals, half-duplex
  Link-layer reliability
  Waiting for fixed periods of time to transmit despite idle medium
  Explicit reservation (RTS/CTS), resulting in “taking turns”

## Slide 10: Multimedia transfers
Streaming (ex: Netflix) and conversational (ex: Skype) media
Peculiar characteristics:
  Delay-sensitivity, loss tolerance, varying quality levels for same data
Application-level adaptations:
  Client-side buffering
  Adaptive playout
System-level adaptations:
  Relay-based routing

## Slide 11: The big picture
Computer networks are a stack of layers
  Built that way for modularity
  Each layer does one set of functions very well
  Each layer depends on the layers beneath it
  But modularity can sometimes result in inefficiency
Many general and useful principles
  Borrowed from real life (ex: listen before you speak)
  Borrowed from systems in general (ex: use indirection for flexibility)
  Applicability goes the other way as well (ex: how to meter freeway ramps)