## Slide 1: The Link Layer: Addressing, Error Detection, & Correction
CS 352, Lecture 19, Spring 2020
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 2: Course announcements
Project 3 released
Ensure you attend recitation this week
  Avoid setup issues by walking together with the TA
  Resolve any issues by asking TAs right there
  Download (large) mininet VM and install VirtualBox before the recitation
Quiz 7 due next Tuesday
Final exam dates shifted slightly
  The exam window is now May 7 @ 7 PM to May 12 @ 7 PM
  Conditions and honor code same as mid-term 2
  Covers all lectures
  All multiple-choice questions

## Slide 3: Network layer: the big picture
The network layer provides connectivity between Internet hosts
  Split into control plane and data plane
Data plane: the IP protocol
  Supported by DHCP, ICMP, NATs
  Routers implement data plane through ports + fabric + queues
Control plane: routing protocols
  Link state: flooding + centralized information + independent computations across routers
  Distance vector: neighbor exchange + decentralized + dependent computations across routers
  Path vector: flooding + decentralized + policy-based dependent computations across routers
Quality of service: isolation, work conservation
  Shaping vs. policing; leaky buckets vs. token buckets

## Slide 4: The Link layer
Application
Transport
Network
Link layer
…
FTP
HTTP
SMTP
DNS
TCP
UDP
IP
802.11
802.3
ATM
HTTPS
Ethernet

## Slide 5: Link layer: introduction
terminology:
hosts and routers: nodes
communication channels that connect adjacent nodes along communication path: links
  wired links
  wireless links
  LANs
layer-2 packet: frame, encapsulates datagram
data-link layer has responsibility of
transferring datagram from one node
to physically adjacent node over a link

## Slide 6: Link layer: context
datagram transferred by different link protocols over different links:
  e.g., Ethernet on first link, frame relay on intermediate links, 802.11 on last link
each link protocol provides different services
  e.g., may or may not provide reliability over link
transportation analogy:
trip from Piscataway to Lausanne
  limo: Piscataway to JFK
  plane: JFK to Geneva
  train: Geneva to Lausanne
tourist = datagram
transport segment (road/flight/rail) = communication link
transportation mode (car/plane/train) = link layer protocol
travel agent = routing algorithm

## Slide 7: Where is the link layer implemented?
in every host
link layer implemented in “adapter” (aka network interface card NIC) or on a chip
  Ethernet card, 802.11 card; Ethernet chipset
  implements link, physical layer
Adapter attaches into host’s system buses (PCI)
Link layer: a combination of hardware, software, firmware
controller
physical
transmission
cpu
memory
host
bus
(e.g., PCI)
network adapter
card
application
transport
network
link
link
physical

## Slide 8: Adapters communicating
sending side:
  encapsulates datagram in frame
  adds reliability/error checking bits
receiving side
  Check for errors
  extracts datagram, passes to upper layer at receiving side (usually: link layer address must match)
controller
controller
sending host
receiving host
datagram
datagram
datagram
frame

## Slide 9: Link layer services
Encoding
  convert bits to signals and recover bits from received signals
framing, link access:
  encapsulate datagram into frame, adding header, trailer
  channel access if shared medium
  “MAC” addresses used in frame headers to identify source, destination
    different from IP address!
reliable delivery between adjacent nodes
  we learned how to do this already (chapter 3)!
  seldom used on low bit-error link (fiber, some twisted pair)
  wireless links: high error rates
    Q: why both link-level and end-end reliability?

## Slide 10: Encoding
Signals propagate over a physical medium
  modulate electromagnetic waves
  e.g., vary voltage
Encode binary data onto signals
  e.g., 0 as low signal and 1 as high signal
  known as Non-Return to zero (NRZ)
  Problem: consecutive 1s and 0s, noise levels
Bits
NRZ
0
0
1
0
1
1
1
1
0
1
0
0
0
0
1
0

## Slide 11: Encodings (cont’d)
Bits
NRZ
Clock
Manchester
NRZI
0
0
1
0
1
1
1
1
0
1
0
0
0
0
1
0
Manchester encoding: +ve transition  0; -ve transition  1
XOR(bit,clock)

## Slide 12: Error detection
EDC = Error Detection and Correction bits (redundancy)
D = Data protected by error checking, may include header fields
Error detection not 100% reliable!
  protocol may miss some errors, but rarely
  larger EDC field yields better detection and correction
otherwise

## Slide 13: Parity checking
single bit parity:
detect single bit errors
two-dimensional bit parity:
detect and correct single bit errors
0
0

## Slide 14: Internet checksum (review)
sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless?
goal: detect “errors” (e.g., flipped bits) in transmitted packet (note: used at transport layer only)

## Slide 15: Cyclic redundancy check
more powerful error-detection coding
view data bits, D, as a binary number
choose r+1 bit pattern (generator), G
goal: choose r CRC bits, R, such that
  <D,R> exactly divisible by G (modulo 2)
  receiver knows G, divides <D,R> by G. If non-zero remainder: error detected!
  can detect all burst errors less than r+1 bits
widely used in practice (Ethernet, 802.11 WiFi, ATM)

## Slide 16: CRC example
want:
  D.2r XOR R = nG
equivalently:
  D.2r = nG XOR R
equivalently:
if we divide D.2r by G, want remainder R to satisfy:
R = remainder[ ]
D.2r
G

## Slide 17: ARP
How to get a MAC address for an IP address?

## Slide 18: ARP: Address Resolution Protocol
By default, NICs only pass on packets destined to their destination MAC address to the higher layers
In a broadcast-based LAN, each source needs to know its destination’s MAC address
After a packet reaches a router, the link layer header needs to be added to reflect the destination host on that link
ARP returns a link layer address when given an Internet address
Communication requires IP  MAC address translation

## Slide 19: ARP packet format
Hardware type: ex: Ethernet (1)
Hardware address length: 6 octets
Protocol Type: ex: IPv4 0x0800 (requesting IPv4 addr)
Protocol address length: 4 octets
Opcode ARP request:1
Opcode ARP reply:2

## Slide 20: ARP operation
Ethernet Address:
05:23:f4:3d:e1:04
IP Address:
128.195.1.20
Ethernet Address:
98:22:ee:f1:90:1a
IP Address:
128.195.1.38
Ethernet Address:
12:04:2c:6e:11:9c
IP Address:
128.195.1.122
Wants to transmit
to 128.195.1.38
ARP
ARP packet
containing “128.195.1.38?”
Ignored
Answered
Proto=IPv4
0x0800
Sender H/W address
Sender IP address
Target H/W address
target IP address
Oper=1